## Slide 1
COURSE PROJECT
Reinforcement Learning
for Adaptive Cruise Control
01 / 16
A transparent tabular policy, classical baselines, and a braking-distance guard
Automotive technology project
Team members: add names
Simulation evidence · literature synthesis · engineering limits
Notes: Opening: We built a compact longitudinal ACC simulation to test whether a small, transparent Q-learning policy adds value when it is placed around a conventional controller. The project compares it with CTG-PID and a simplified MPC baseline, then examines an RSS-inspired action guard. State clearly that the results are simulation evidence.

## Slide 2
01 · ENGINEERING CONTEXT
ACC couples vehicle dynamics, comfort and following distance.
AUTOMOTIVE TECHNOLOGY · ACC + RL
02
An ACC controller must regulate the ego vehicle while the lead vehicle changes speed.
01
Track a chosen time gap
Spacing changes as ego speed changes.
02
Respond to braking
Actuator lag delays the vehicle response.
03
Avoid harsh control
Acceleration and jerk affect comfort.
04
Limit disturbance growth
A follower can amplify a traffic wave.
The project scope: longitudinal car-following only.
Notes: Explain the automotive motivation in engineering terms. ACC is not just a machine-learning benchmark: desired following distance varies with speed, vehicle acceleration is bounded, actuators have delay, comfort matters, and vehicle strings can transmit disturbances. Our prototype deliberately isolates longitudinal following; it has no steering, perception or lane-change geometry.

## Slide 3
02 · LITERATURE
Three research threads shape the question.
AUTOMOTIVE TECHNOLOGY · ACC + RL
03
CLASSICAL ACC
Bageshwar et al. (2004)
Predictive control for transitional maneuvers.
Li et al. (2011)
Multi-objective ACC MPC.
He et al. (2019)
Review of experimental-vehicle strategies.
Strong baselines; real-vehicle evidence remains comparatively limited.
LEARNED FOLLOWING
Desjardins & Chaib-draa (2011)
RL for cooperative ACC.
Zhu et al. (2018, 2020)
Naturalistic car-following and safety/comfort objectives.
Lin et al. (2021)
DRL vs MPC for ACC.
Objectives and evidence settings vary across papers.
SAFETY METHODS
Ames et al. (2014)
CBF-QP applied to ACC.
RSS (2017) · shielding (2018)
Explicit safety rules / action filtering.
Hailemichael et al. (2022)
Safety filtering for RL-based ACC.
Assurance depends on explicit models and assumptions.
Notes: Synthesize by research question. Classical control papers study tracking and transitions; RL studies may reproduce human trajectories, coordinate vehicles, or optimize traffic flow; safety papers define different kinds of filters or formal conditions. Do not treat their results as directly interchangeable. References: Bageshwar et al. 2004, https://doi.org/10.1109/TVT.2004.833625; Li et al. 2011, https://doi.org/10.1109/TCST.2010.2049203; He et al. 2019, https://doi.org/10.1016/j.ifacol.2019.09.004; Desjardins & Chaib-draa 2011, https://doi.org/10.1109/TITS.2011.2157145; Zhu et al. 2018, https://doi.org/10.1016/j.trc.2018.10.024; Zhu et al. 2020, https://doi.org/10.1016/j.trc.2020.102662; Lin et al. 2021, https://doi.org/10.1109/TIV.2020.3012947; Ames et al. 2014, https://doi.org/10.1109/CDC.2014.7040372; Shalev-Shwartz et al. 2017, https://arxiv.org/abs/1708.06374; Alshiekh et al. 2018, https://doi.org/10.1609/AAAI.V32I1.11797; Hailemichael et al. 2022, https://doi.org/10.1016/j.ifacol.2022.10.276.

## Slide 4
03 · RESEARCH DESIGN
Can tabular RL improve a CTG controller without hiding the control logic?
AUTOMOTIVE TECHNOLOGY · ACC + RL
04
We test a small learned acceleration residual, then compare it with CTG-PID and simplified MPC.
RUBRIC NOTE
30–35 marks
for the literature review
10 marks
for own work / findings
30–35 marks
for actual research
13
The supplied guide suggests about 13 papers.
The 30–35 figures are mark bands, not required paper counts.
Project contribution: transparent residual Q + matched evaluation + honest limits.
Notes: The attached course guide allocates 30–35 marks to the literature review, 10 to own work/findings, and 30–35 to actual research. It separately suggests about 13 papers. We interpreted the mark values correctly and designed a focused review rather than assuming the team needs 30–35 papers.

## Slide 5
04 · ARCHITECTURE
The learned action is a small residual inside an automotive control loop.
AUTOMOTIVE TECHNOLOGY · ACC + RL
05
Lead profile
speed + braking
scenario
Observation
gap error · closing speed
ego speed · acceleration
CTG-PID
nominal time-gap
feedback command
Q table
discrete residual
acceleration
Action guard
RSS-inspired
braking margin
Actuator + ego vehicle
first-order lag · drag · rolling resistance · bounded acceleration
ego motion
A zero residual leaves CTG-PID in charge for tied or unvisited state bins.
Notes: Walk left to right. The lead profile sets speed; state features describe the car-following situation; CTG-PID supplies the nominal acceleration; Q chooses a discrete residual; an optional braking-distance guard can clip the command; actuator and longitudinal plant determine next state. In unseen or tied table states the action is zero residual. This fallback does not prove safety.

## Slide 6
05 · MODEL AND POLICY
A compact model keeps the experiment inspectable.
AUTOMOTIVE TECHNOLOGY · ACC + RL
06
VEHICLE MODEL
Δt = 0.1 s · mass = 1,500 kg
actuator τ = 0.35 s
acceleration command = −6 to +2.5 m/s²
TIME-GAP POLICY
d* = 5 m + 1.3 v
Five state features
gap error
closing speed
ego speed
actual ego acceleration
estimated lead acceleration
Seven residual actions
−1.2 −0.6 −0.25 0 +0.25 +0.6 +1.2 m/s²
6,000 episodes · α = 0.12 · γ = 0.985
The reward penalizes gap error, relative speed, acceleration, jerk, negative braking margin and collision.
Notes: Describe the 10 Hz longitudinal point-mass model and the chosen time-gap policy. The Q-table has five discretized state features and seven acceleration residuals. The reward combines normalized tracking, relative-speed, acceleration and jerk penalties, a soft negative-margin shaping cost and a large collision penalty. The discretization is intentionally inspectable but many bins are never visited; the chosen action granularity is a limitation. Q-learning update follows Watkins and Dayan (1992), https://doi.org/10.1007/BF00992698.

## Slide 7
06 · EVALUATION PROTOCOL
Matched controllers, five scripted scenarios, eight seeds per cell.
AUTOMOTIVE TECHNOLOGY · ACC + RL
07
TRAINING
6,000 episodes
steady · smooth wave · moderate brake
IN-DISTRIBUTION
3 scenarios
steady · wave · brake
HOLDOUT
2 stresses
synthetic gap drop + brake
higher-speed emergency brake
CTG-PID
MPC
Residual Q
Q + guard
5 scenarios × 4 controllers × 8 seeds = 160 episodes
Same scenario and seed are used across controllers. The cut-in is a 22 m instantaneous gap reduction, not lane-change geometry.
Notes: Explain the protocol: training includes steady, wave and moderate braking; evaluation has three in-distribution profiles and two holdouts. Each of the five scenarios runs against four controllers for eight matched seeds, totalling 160 episodes. The cut-in is modeled as an instantaneous 22 m gap decrease at eight seconds followed by sharper braking. That is a deliberately simplified stress test, not a lane-change model.

## Slide 8
07 · RESULTS · TRACKING
MPC gives the lowest gap error in both evaluation groups.
AUTOMOTIVE TECHNOLOGY · ACC + RL
08
Chart: Episode gap RMSE (m) · mean across scenarios and seeds
| CTG-PID | MPC | Residual Q | Q + guard
In-distribution (24 episodes) | 2.36 | 1.58 | 2.54 | 2.54
Holdout (16 episodes) | 3.55 | 2.43 | 4.9 | 3.92
Lower tracking error does not by itself mean safer or more comfortable control.
Notes: These are mean episode-level gap RMSE values. In-distribution averages three scenario families × eight seeds (24 episodes); holdout averages two × eight (16). MPC is lowest: 1.58 m in-distribution and 2.43 m holdout. Residual Q is 2.54 m and 4.90 m, respectively. CTG-PID is 2.36 m and 3.55 m. Q+guard equals Q in-distribution because no guard interventions occurred there. This is project simulation data.

## Slide 9
08 · RESULTS · COMFORT
The learned corrections add jerk; the guard adds more on holdout.
AUTOMOTIVE TECHNOLOGY · ACC + RL
09
Chart: Mean absolute jerk (m/s³)
| CTG-PID | MPC | Residual Q | Q + guard
In-distribution | 0.207 | 0.271 | 0.504 | 0.504
Holdout | 0.277 | 0.587 | 0.726 | 0.902
Comfort signal
Q adds discrete action changes on top of a smooth nominal controller.
Q + guard
0.902 m/s³ holdout mean |jerk|, versus 0.726 for unfiltered Q.
Notes: Jerk is a rough proxy for longitudinal smoothness, not a complete measure of ride comfort. CTG-PID has lower mean absolute jerk than Q in both groups. The guard can create sharp command changes; across the two holdouts its mean episode-level jerk rises from 0.726 to 0.902 m/s³. In the training-like group the guard never intervened, so Q and Q+guard match.

## Slide 10
09 · RESULTS · HOLDOUT STRESS
The synthetic cut-in exposes the filter’s safety–comfort trade-off.
AUTOMOTIVE TECHNOLOGY · ACC + RL
10
Chart: Minimum gap in cut-in runs (m) · mean of 8 seeds
| CTG-PID | MPC | Residual Q | Q + guard
Minimum gap | 6.76 | 11.26 | 3.41 | 9.14
Q TIME WITH TTC < 2 S
3.13%
Q + guard: 0% in these runs
GUARD INTERVENTIONS
32.9 / run
8.22% of cut-in time steps
The modeled cut-in is an instantaneous 22 m gap drop; no lane-change dynamics.
Notes: In the synthetic cut-in, residual Q had average minimum gap 3.41 m and TTC under two seconds for 3.125% of closing samples; the per-episode mean is displayed as 3.13%. The RSS-inspired guard increased average minimum gap to 9.14 m and the TTC-below-two indicator to zero, but changed about 32.9 actions per run (8.22% of steps) and increased jerk. This filter is a simplified braking-margin heuristic, not full RSS, a CBF proof or a certification. The cut-in itself is a sudden 22 m gap drop at 8 seconds, not a lane-change model.

## Slide 11
10 · RESULTS · DISTURBANCE RESPONSE
In one four-car pulse, Q slightly amplifies the final speed deviation.
AUTOMOTIVE TECHNOLOGY · ACC + RL
11
Chart: Last follower / leader peak speed deviation
| CTG-PID | MPC | Residual Q | Q + guard
Peak amplification ratio | 0.735 | 0.633 | 1.04 | 1.04
Read the ratio
< 1 · this pulse attenuates
> 1 · this pulse amplifies
4 vehicles
one 32 s test
−2 m/s² leader pulse for 1.2 s, then recovery
A diagnostic for one pulse—not a general string-stability proof.
Notes: The ratio is the last follower’s peak speed deviation divided by the leader’s peak deviation, which was 2.4 m/s. CTG-PID is 0.735, MPC 0.633, and both Q variants 1.040. This selected test suggests attenuation for CTG/MPC and slight amplification for Q. It is a single 4-car, 32-second pulse test, not formal proof of string stability across all frequencies, delays or configurations. References: Swaroop & Hedrick (1996), https://doi.org/10.1109/9.486636; Ploeg et al. (2014), https://doi.org/10.1109/TITS.2013.2291493.

## Slide 12
11 · LITERATURE SYNTHESIS
The evidence supports testing trade-offs, not assuming RL wins.
AUTOMOTIVE TECHNOLOGY · ACC + RL
12
01
Classical methods set a clear reference.
MPC can exploit a model and objective; feedback control gives a simple nominal policy.
02
RL results depend on what is learned.
Trajectory imitation, CACC coordination and traffic-wave damping answer different questions.
03
Safety filters inherit their assumptions.
A numerical action guard is weaker evidence than a verified model/specification with explicit guarantees.
Our niche: an inspectable residual policy, evaluated against transparent baselines and explicit holdouts.
Notes: The literature suggests a careful comparison. ACC/MPC work motivates model-based baselines and multi-objective evaluation. RL studies differ in whether they target trajectories, cooperative platoons or network flow. Safety filtering spans heuristics, shields, RSS-style models and formal CBF methods. Our project is scoped to transparent integration and matched simulation, not a new safety proof. Cite Lin et al. 2021, Watkins & Dayan 1992, Ames et al. 2014, Alshiekh et al. 2018, and ISO 21448:2022 for the safety-development context.

## Slide 13
12 · OWN WORK
The first Q policy failed; the redesign made the baseline explicit.
AUTOMOTIVE TECHNOLOGY · ACC + RL
13
ABSOLUTE ACTION PILOT
15.20 m
in-distribution gap RMSE
1 / 24
episodes had a collision
RESIDUAL Q REDESIGN
CTG-PID action
+ one of seven learned corrections
zero residual on ties / unvisited bins
FORMAL RESULT
2.54 m
Q gap RMSE
24 in-distribution episodes
2.36 m
CTG-PID gap RMSE
24 in-distribution episodes
The pilot is archived; final results use the revised, separately trained table.
Notes: This slide shows the project’s own iteration. Absolute-action tabular Q performed badly in a pilot, with 15.20 m in-distribution RMSE versus 2.36 CTG and 1.58 MPC, and one collision among 24 in-distribution trials. We retained the pilot artifacts and changed to residual Q: CTG-PID supplies the nominal action, and the learner selects a bounded residual. Formal residual Q is much closer at 2.54 m, but still not better than CTG or MPC and has higher jerk.

## Slide 14
13 · CONCLUSION
For this setup, classical control remains the stronger reference.
14 / 16
TRACKING
MPC had the lowest gap RMSE.
COMFORT
Residual Q increased mean absolute jerk.
HOLDOUT
The guard improved Q’s cut-in TTC/gap indicators, with frequent action changes.
This is a reproducible teaching simulation—not a vehicle safety claim.
Next: broaden uncertainty and scenarios; compare against a formal safety filter.
Notes: Close by answering the question directly. The compact residual Q policy was transparent, but did not beat CTG-PID or simplified MPC on tracking or jerk. The braking-distance guard improved selected holdout indicators at a comfort/intervention cost. The main contribution is a reproducible, honest comparison and a clear next research plan—not evidence that the policy is ready for a car.

## Slide 15
REFERENCES · 1 OF 2
ACC control and reinforcement learning
AUTOMOTIVE TECHNOLOGY · ACC + RL
15
Swaroop, D., & Hedrick, J. K. (1996). String stability of interconnected systems. IEEE Transactions on Automatic Control, 41(3), 349–357. DOI: 10.1109/9.486636.
Bageshwar, V. L., Garrard, W. L., & Rajamani, R. (2004). Model predictive control of transitional maneuvers for adaptive cruise control vehicles. IEEE Transactions on Vehicular Technology, 53(5), 1573–1585. DOI: 10.1109/TVT.2004.833625.
Li, S. E., Li, K., Rajamani, R., & Wang, J. (2011). Model predictive multi-objective vehicular adaptive cruise control. IEEE Transactions on Control Systems Technology, 19(3), 556–566. DOI: 10.1109/TCST.2010.2049203.
He, Y. et al. (2019). Adaptive cruise control strategies implemented on experimental vehicles: A review. IFAC-PapersOnLine, 52(5), 21–27. DOI: 10.1016/j.ifacol.2019.09.004.
Watkins, C. J. C. H., & Dayan, P. (1992). Q-learning. Machine Learning, 8, 279–292. DOI: 10.1007/BF00992698.
Desjardins, C., & Chaib-draa, B. (2011). Cooperative adaptive cruise control: A reinforcement learning approach. IEEE Transactions on Intelligent Transportation Systems, 12(4), 1248–1260. DOI: 10.1109/TITS.2011.2157145.
Zhu, M., Wang, X., & Wang, Y. (2018). Human-like autonomous car-following model with deep reinforcement learning. Transportation Research Part C, 97, 348–368. DOI: 10.1016/j.trc.2018.10.024.
Zhu, M. et al. (2020). Safe, efficient, and comfortable velocity control based on reinforcement learning for autonomous driving. Transportation Research Part C, 117, 102662. DOI: 10.1016/j.trc.2020.102662.
Lin, Y., McPhee, J., & Azad, N. L. (2021). Comparison of deep reinforcement learning and model predictive control for adaptive cruise control. IEEE Transactions on Intelligent Vehicles, 6, 221–231. DOI: 10.1109/TIV.2020.3012947.
Notes: These references support the ACC/MPC, string-stability and RL claims in the talk. For paper-level results consult the full publication, not only this slide.

## Slide 16
REFERENCES · 2 OF 2
Safety filtering, metrics and standards
AUTOMOTIVE TECHNOLOGY · ACC + RL
16
Ames, A. D. et al. (2014). Control barrier function based quadratic programs with application to adaptive cruise control. IEEE CDC. DOI: 10.1109/CDC.2014.7040372.
Shalev-Shwartz, S., Shammah, S., & Shashua, A. (2017). On a formal model of safe and scalable self-driving cars. arXiv:1708.06374.
Alshiekh, M. et al. (2018). Safe reinforcement learning via shielding. AAAI, 32(1), 2669–2678. DOI: 10.1609/AAAI.V32I1.11797.
Ploeg, J., van de Wouw, N., & Nijmeijer, H. (2014). Controller synthesis for string stability of vehicle platoons. IEEE T-ITS, 15(2), 854–865. DOI: 10.1109/TITS.2013.2291493.
Hailemichael, G. et al. (2022). Safety filtering for reinforcement learning-based adaptive cruise control. IFAC-PapersOnLine, 55(24). DOI: 10.1016/j.ifacol.2022.10.276.
ElSamadisy, M. et al. (2024). Safe, efficient, and comfortable RL-based car-following for AVs with an analytic safety guarantee and dynamic target speed. TR Record, 2678(1), 643–661. DOI: 10.1177/03611981231171899.
Vogel, K. (2003). A comparison of headway and time to collision as safety indicators. Accident Analysis & Prevention, 35(3), 427–433. DOI: 10.1016/S0001-4575(02)00022-2.
ISO 15622:2018. Intelligent transport systems — Adaptive cruise control systems — Performance requirements and test procedures. iso.org/standard/71515.html.
ISO 21448:2022. Road vehicles — Safety of the intended functionality (SOTIF). iso.org/standard/77490.html.
Our braking-distance guard is RSS-inspired; it is not a formal RSS, CBF, SOTIF assessment or certification.
Notes: Safety terminology references: Ames et al. 2014 is an ACC-specific CBF-QP study; RSS is a safe-distance model; shielding filters actions against modeled specifications; ISO 15622 covers ACC performance requirements and test procedures; ISO 21448 provides a SOTIF framework. Our simplified guard does not implement or inherit any formal guarantee from these sources.